Installing HID bulbs in your 04-05 Rhino factory housing:

- First, remove from the stock housing (unplug)

- Then, remove the stock bulbs by pushing in the tabs that are inside the housing next to the bulb. The bulb will pop out. Be careful not to break the tabs.

- Next, take a hacksaw or a band saw, and cut off the end of the stock housing at the base, below plastic wings that remove the bulb from the fixture. (wires and all)

- Disregard the bulb and the stock wiring. (it won’t be used)

- Using a Dremel, Uni-Bit or round file, open the inner diameter 1/16” at the base of the bulb fixture.

- Install the HID wires and the bulb from the top of the stock housing or fixture (then the HID bulb will snap into stock base clips)

- Install the end connectors. (supplied with kit)

- Before crimping the supplied connectors, make sure that these connectors will plug into the opposite power and ground properly.

- Fill the base with silicone at the bottom. (keeps moisture and sand, etc. out)