04, 05, 06 Polaris Ranger installation instructions for HID retrofit upgrade kit.

Please note: This kit requires the use of solder-less connectors to factory loom. It “will not” plug into a factory harness.

- First, start by removing the factory Polaris bulbs, and replace them with your Vision X HID bulbs.
 (put a small dab of silicone on the outer lip of the bulb after you have installed it.)

- Then, mount each Vision X ballast to the left or right of the stock upper shock mount.  Please note: You will be required to drill and bolt through plastic skirt (we also suggest a little silicone on the back of the ballast, and vibration dampener as well.)

- At this time, you will need to peal the protective loom back from the Polaris loom about 4” or so. Once this is done, cut the stock connector and the bulb off, (the 4” is in case you decide to go back to the stock bulbs).

- There is a Yellow/Brown and Green Polaris power wire that you will see. However, you will “Not” use the Yellow Polaris wire for this installation, because the high beam is not used in HID.

- At this time, you will now want to splice the Vision X Ballast to the stock Polaris wire loom.

- Then, splice the:

* Yellow wire at the Vision Ballast to the Polaris Green wire.

*Black wire at the Vision X ballast to the Polaris Brown wire.

Please duplicate for both sides (passenger and driver side)

- The yellow Polaris wire is the high beam power, and you won’t have or need high beam, so don't worry about this.

Now that the bulbs are in, and the Ballasts are wired to the Polaris loom, lower the hood about half way closed and plug the bulbs into the ballasts.

“Note” In order to open the hood completely, you will have to disconnect the bulbs every time.  If you activate “High Beams” the lights will automatically shut off.

Copyright Vision Motor Sports ©2008