07 – 08 Polaris RZR installation instructions

Installing the new HID bulb:

- First remove the factory bulbs from headlight housing by twisting ¼ turn and pulling outward. Then unplug the bulb from the wire harness and store it for possible future use. Now you are ready to install new Vision “X” HID bulb. Be very careful not to touch the glass part of the bulb. If you do please wipe the bulb clean with an alcohol solution.

Installing the new Vision “X” HID Starter Ballasts:

- First you want to remove the front truck area hood. Then place one starter ballast (with the connectors facing upwards) in each lower corner of the trunk space area. 
(Do not use mounting 3M tape yet). Next drill a 7/8” hole through the plastic truck area in the upper left and right hand sides of the inner trunk area, so that both the power and the output wire can fit through.

Wiring up the lights and ballast:

- Now you want to feed the 2 power and ground wires through the trunk opening one at a time, and plug into bulb at the back of headlight housing. Now take the supplied 10” wire harness and plug one end into the factory wire harness (for power) and feed the other end through the 7/8” hole and plug it into the Vision X HID Ballast. After the power wire and bulb are connected, start up the RZR and make sure they light up.

Mounting the Ballast:

- First you want to remove the protective paper from both sides of the 3M pad and stick it to the bottom of the ballast. Then place it in the trunk area, (make sure the area is clean) and use the supplied zip ties to tie up any extra length that might interfere with any moving parts. The trunk area is not sealed from the factory but if you choose you can seal up the 7/8” opening with a little silicone. The weather will not affect our Vision X parts.