07, 08, 09 Polaris Ranger installation instructions

Installing the new HID bulb:

- First, remove the factory bulbs from the headlight housing by twisting ¼ turn and pulling outward. Then unplug the bulb from the wire harness and store it for possible future use. Now you want to install the new Vision “X” HID bulb, while being very careful not to touch the glass part of the bulb. If you do touch the glass part of the bulb, please be sure to wipe it clean with an alcohol solution.

Installing the new Vision “X” HID Starter Ballasts:

- Now you want to remove the front truck area hood, and place one starter ballast (with the connectors facing upwards) in each lower corner of the trunk space area (do not use the mounting 3M tape yet). Next, drill a 7/8” hole through plastic truck area in the upper left and right hand side of the inner trunk area, so that both the power and output wire can fit through.

Wiring up the lights and ballast:

- Next you want to feed the 2 power and ground wires through the trunk opening one at a time, and plug into the bulb at the back of headlight housing. Next take the supplied 10” wire harness and plug one end of it into the factory wire harness (for power) and feed the other end through the 7/8” hole, and plug it into the Vision X HID Ballast. After the power wire and the bulb are connected, start up the Ranger and make sure that they light up.

Mounting the Ballast:

- First remove the protective paper from both sides of the 3M pad and stick to the bottom of the ballast. Then place it in the trunk area (make sure the area is clean). Now you want to use the supplied zip ties to tie up any extra length that might interfere with any moving parts. The trunk area is not sealed from the factory but if you choose you can seal up the 7/8” opening with silicone, the weather will not affect our Vision X parts.