2007 - Current Polaris RZR    &    2009 - Current Polaris Ranger XP

Installing the new HID bulb:

- First, remove the factory bulbs from the headlight housing by twisting ¼ turn and pulling outward. Then unplug the bulb from the wire harness and store it somewhere safe for possible future use. Now install the new Vision X HID bulb being very careful not to touch the glass part of the bulb. If you do touch the glass part of the bulb,  please wipe clean with an alcohol solution.

Installing the new Speed Industries HID Starter Ballasts:

- First you want to remove the front truck area hood, and place one starter ballast (with the connectors facing upwards) in each lower corner of the trunk space area. (don’t use the mounting 3M tape just yet.) Next drill a 7/8” hole through the plastic truck area in the upper left and right hand sides of the inner trunk area so both the power and output wire can fit through.

Wiring up the lights and ballast:

- Now you want to feed the 2 power and ground wires through the trunk opening, one at a time, and plug into bulb at the back of the headlight housing. Then, take the supplied 10” wire harness, and plug one end into the factory wire harness (for power) and feed the other end through the 7/8” hole, and plug into the Vision X HID Ballast. After the power wire and the bulb are connected, start the vehicle up and make sure that they light up.

Mounting/Wiring:

- Now that you are ready to mount/wire, remove the protective paper from both sides of the 3M pad and stick it to the bottom of the ballast, then place it in the trunk area. (make sure the area is clean.) Now, use the supplied zip ties to tie up any extra length that might interfere with any moving parts. The trunk area is not sealed from the factory but if you choose you can seal up the 7/8” opening with a little silicone. The weather will not affect our Vision X parts.

- Again, this application has multiple vehicles it can fit so please be patient and allow approximately 1-2 hrs to complete your install.

- Plug black female plug on relay harness into driver side of the factory harness bulb plug using the provided vehicle adapter plug and zip tie remaining passenger factory harness bulb plug out of the way, as you will not need to use this plug anymore.

- Plug the (2) male output plugs from the relay harness into the ballasts making sure the clips are facing the outside of the ballast.

- Run + and – ring terminals on relay harness to battery under driver’s seat and install onto pertinent battery posts, red wire with fuse to red positive (+) terminal on battery and black wire to black negative (-) terminal.

- After you install our Vision X system, please make sure all wires are zip tied tightly, and nothing is exposed or left hanging down.