Installing 2007 and Up Yamaha Rhino conversion:

- First, remove the factory bulb by twisting the stock bulb to the left ¼ turn while pushing inwards.

- Disconnect from the stock wiring harness

- Install the Vision X bulb into the stock headlight housing, being careful not to touch the glass bulb with your fingers. If you do just wipe clean with a dry clean cloth.

- Install the Vision X starter ballast in a place where it will stay clear or debris. Then use a little silicone bead on the back of the ballast to absorb some of the vibrations.

Wiring up Harness:

- Plug black female plug on relay harness into driver side of the factory harness bulb plug using the provided vehicle adapter plug and zip tie remaining passenger factory harness bulb plug out of the way, as you will not need to use this plug anymore.

- Plug the (2) male output plugs from the relay harness into the ballasts making sure the clips are facing the outside of the ballast.

- Run + and – ring terminals on relay harness to battery under driver’s seat and install onto pertinent battery posts, red wire with fuse to red positive (+) terminal on battery and black wire to black negative (-) terminal.

- After you install our “Speed” system, please make sure all wires are zip tied tightly, and nothing is exposed or left hanging down.

- You’re done!

Have fun.