Installation instructions for Arctic Cat Prowler

• Open the front hood, and remove the outer bulbs from the stock headlight fixture.

• Install the Vision X HID bulbs where the stock ones used to be.

• Mount the ballast in the front, behind the stock skid plate. Make sure that the length is OK, from the ballast to the bulb, and not to short. You can use self tapping screws, however you should also add a little silicone to each screw. It helps prevent the screw from backing out under vibrations. You should still check the screws occasionally though.

• Plug Vision X Bulbs into Vision X Ballast

• Wiring and ballast:

- Plug the black female plug on the relay harness into the driver side of the factory harness bulb plug using the provided vehicle adapter plug. Now zip tie the remaining passenger factory harness bulb plug out of the way, as you will not need to use this plug anymore.

- Plug the (2) male output plugs from the relay harness into the ballasts making sure the clips are facing the outside of the ballast.

- Run + and – ring terminals on the relay harness to the battery under the driver’s seat, and install onto pertinent battery posts. Red wire with fuse to red positive (+) terminal on battery and black wire to black negative (-) terminal.

- After you install your Vision X system, please make sure that all wires are zip tied tightly, and nothing is exposed or left hanging down.

• “Note” This kit is used on the LOW beam of the stock lights, so when you activate the high beam on the dash, both the HID and the high beam will come on. This is no problem, and the high beam will be barely visible with the LOW beam HID lights on.

Thank you

VisionXwholesale.com