HID-116 installation instructions

Installing  the HID Kit: (04-05 Rhino upgrade #06RH  is needed.)

First, remove the factory halogen bulbs from the stock housings,  and install the new supplied HID Bulbs. Do not touch these bulbs with your fingers, if you do, wipe thoroughly with soft clean cloth, and alcohol solution.  Leave the factory bulbs hanging there for later instructions. (for 04-05 Rhino, Install the upgrade housings before you start this installation)

Now plug the bulb's red and white wires into the red and white wires off the supplied ballast. After this is done, find a position to mount each ballast that will be out of the way of moving parts. You cannot extend these power wires at all!

After you find a suitable place to mount the ballasts, use the supplied hardware to do so, then on some applications (Rhino’s etc) you will need to unplug the power wire from loom, on others you will need to unplug bulb at the end of the factory connector. (near bulb housing) Use the supplied Vision X power lead to plug into each Vision X ballast. The opposite end will either plug into stock harness or into where the stock halogen bulb is plugged in.

Again this application has multiple vehicles, so it can fit. Therefore, please be patient and allow approximately 1-2 hrs to complete the install.

Before using the wire ties, please start the vehicle and test. If the lights don’t turn on, check the power lead (oval) into ballast, and make sure it’s not installed upside down (180 degrees out). If the lights flicker or blow the factory fuse and then turn off, you will need to use the Vision X relay harness provided. The flicker or fuse popping can be caused by lack of power or a tired battery, the relay harness will fix this.

After you get the lights to work, tie up all loose wires and enjoy!