HID-226 installation instructions

First, remove the factory halogen bulbs from the stock housings, then  install the new supplied HID Bulbs. Do not touch these bulbs with your fingers, if so wipe thoroughly with soft clean cloth. Once this is done, leave the factory bulbs hanging there for later use.

Now plug the bulb red and white wires into the red and white wires off the supplied ballast. After this is done, find a position to mount each ballast, that will be out of the way of moving parts. You cannot extend these power wires at all!

After you find a place to mount ballasts, use the supplied hardware to do so, then on some applications (Rhino’s etc) you will unplug the power wire from the loom. On others you will need to unplug the bulb at the end of the factory connector (near bulb housing). Use the supplied Vision X power lead to plug into each Vision X ballast, the opposite end will either plug into the stock harness or into where the stock halogen bulb is plugged in.

Again this application has multiple vehicles it can fit, so please be patient and allow approximately 1-2 hrs to install.

Before using the wire ties, please start up your vehicle and test the lights. If your lights don’t turn on check power the lead(oval) into ballast to make sure it’s not installed upside down (180 degrees out). If the lights flicker or blow the factory fuse and then turn off, you will need to use the Vision X relay harness. The flicker or fuse popping can be caused by lack of power or a tired battery, the relay harness will fix this.

After you get the lights to work, tie up all loose wires and enjoy!