Installing HID 336 kit:

- First, remove the factory bulb by twisting the stock bulb to the left ¼ turn while pushing inwards.

- Then, disconnect from stock wiring harness.

- Once the stock bulb is disconnected, install the Vision X bulb into the stock headlight housing, while being very careful not to touch glass bulb with your fingers. If you do, just wipe clean with a dry clean cloth.

- Install the Vision X starter ballast in a place where it will stay clear of debris, use the  supplied brackets to mount the ballast.

- Then plug each power wire (Red) from the bulb to the ballast, and ground (Black) to the ballast using the supplied hardware. Then plug the bulb wires into the ballast, and plug the supplied wire harness into the ballast, and then into the stock headlight wire harness for each side.

- Again, this application has multiple vehicles it can fit. Therefore please be patient and allow approximately 1-2 hrs to install.

- Before using the wire ties, please start up your vehicle and test the lights. If the lights don’t turn on, check the power lead(oval) into ballast to make sure it’s not installed upside down (180 degrees out). If lights flicker or blow the factory fuse and then turn off, you will need to use the Vision X relay harness. The flicker or fuse popping can be caused by a lack of power or a tired battery, the relay harness will fix this.

- After you get the lights to work, tie up all loose wires and enjoy