HID-446 Installation Instructions

Please note: This kit requires the use of solder-less connectors to a factory loom, It will not plug into a stock factory harness.

- First, remove the factory bulbs, and replace them with the Vision X HID bulbs (put a dab of silicone on outer lip of bulb after installed)

- Then mount each of the Vision X ballasts to the left or right side of the stock upper shock mount.  Please note: On some applications you will be required to drill and bolt through a plastic skirt. (we also suggest a little silicone on back of ballast, vibration dampener)

- At this time you will need to peal the protective loom back from the factory loom about 4”. Next, cut the stock connector and the bulb off. (the 4” is in case you decide to go back to stock bulbs).

- The majority of applications that this kit fits have a Yellow/Brown and Green power wires; you will not use the Yellow  wire (High Beam) for this install. The high beam is not used in HID.

- Now, you want to splice the Vision X Ballast to the stock wire loom.

- Splice the:

* Yellow wire at the Vision Ballast to the Green wire

*Black wire at the Vision X ballast to the Brown wire

Please duplicate for both sides (passenger and driver side)

- The yellow  wire is the high beam power; you won’t have or need a high beam.

Now the bulbs are in, and the Ballasts are wired to the loom, some vehicles with a front hood, will only open about half way after this kit is installed, so closed and plug the bulbs into the ballasts.

“Note” In order to open hood completely, you will have to disconnect bulbs every time.  If you activate “High Beams” the lights will shut off.