HID-556 installation instructions

Installing the new HID bulb:

- First, remove the factory bulbs from the headlight housing by twisting ¼ turn and pulling outward. Then, unplug the bulbs from the wire harnesses and store them for possible future use. Now, install new Vision “X” HID bulbs being careful not to touch the glass part of the bulb, if you do please wipe clean with an alcohol solution.

Installing the new Vision “X” HID Starter Ballasts:

- Remove the front truck area hood, place one starter ballast (with connectors facing upwards) in each lower corner of the trunk space area. (don’t use the mounting 3M tape yet). Next, drill a 7/8” hole through the plastic trunk area in the upper left and right hand side of the inner trunk area so that both the power and output wire can fit through.

Wiring up the lights and ballast:

- First feed the 2 power and ground wires through the trunk opening one at a time, and plug into the bulb at the back of the headlight housing. Next, take the supplied 10” wire harness and plug one end into the factory wire harness (for power) and feed the other end through the 7/8” hole, and plug it into the Vision X HID Ballast. After the power wires  and the bulbs are connected, start the vehicle and make sure they light up.

Mounting the Ballast:

- Remove the protective paper from both sides of the 3M pad and stick it to the bottom of the ballast. Then place it in the trunk area (make sure the area is clean). Use the supplied zip ties to tie up any extra length that might interfere with any moving parts. The trunk area is not sealed from the factory, but if you choose you can seal up the 7/8” opening with a few beads of silicone. The weather will not affect our Vision X parts.

- Again this application has multiple vehicles it can fit, therefore please be patient and allow approximately 1-2 hrs for install.

- Before using the wire ties, please start your vehicle and test the lights. If the lights don’t turn on, check the power lead(oval) into ballast to make sure it’s not installed upside down (180 degrees out). If the lights flicker or blow the factory fuse, and then turn off, you will need to use the Vision X relay harness. The flicker or fuse popping can be caused by lack of power or a tired battery. The relay harness will fix this.

- After you get the lights to work, tie up all loose wires and enjoy!