Parts included in kit:

- x  4’ or 3’ LED Bar

- x  Deutsch Wire Pig Tail

- x Spade Connectors Male

- x T-Taps

(6) x 2-Way Zip Tie Mount

(9) x Zip Ties

Installation: (Courtesy/Approach Light Operation)

(Note: your vehicle must be equipped with them from the factory. To test unlock your truck when it is dark and if the reverse light turns on and stays on…you have them..)

- Locate area in Truck Bed where the LED Bar will be mounted.

- Thoroughly clean area using a solution that will not leave a film. Rubbing Alcohol is suggested.

- Hold LED Bar up to the desired area and mark a minimum of 4 points where the 2-Way Zip Tie Mounts will be placed that will hold LED Bar.

- Remove protective film from the 2-Way Zip Tie Mounts and firmly push against the area that you marked.

- Run 1 Zip Tie through each 2-Way Zip Tie Mount, loop around LED Bar, and tighten Zip Tie, making sure the wire end is facing the back of the truck.

Now that your LED Bar is mounted in your desired location you will need to wire it.

- Remove the taillight on the same side as where you mounted the light bar.

- Look for the best way to route wire towards the nearest Tail Light of the vehicle. (Normally under the rail of the bed is an opening that goes directly to the tail light opening)

- The remaining 2-Way Zip Tie Mounts have been provided to mount the visible wire run if necessary.

- Mount wire making sure to secure wire using Provided Zip Ties every 2’ Minimum

- Locate the (+) Positive & (-) Negative Reverse Bulb Wires using a multi meter to test and crimp one T-Tap on each wire. (Note, when testing make sure the vehicle is not running and the emergency brake is on and functioning. One person should always remain in the truck with their foot on the foot brake while testing.)

- Crimp Spade Connectors on Deutsch Pig Tail Wires

- Double check which Reverse Bulb Wire is (+) Positive and  plug Red Wire from Deutsch Pig Tail into the T-Tap on this wire.

- Double check which Reverse Bulb Wire is (-) Negative and  plug Black Wire from Deutsch Pig Tail into the T-Tap on this wire.

- Now it is time to test out your new Truck Bed Light. Set E-Brake to on, turn on Ignition without starting the Vehicle, put Vehicle in Reverse, and look to see the Bed of your Truck Clearly Lit Up! The next time you unlock your truck at night, watch it light up. Press repeatedly to re-light after time out.

WARNING: THIS LIGHT WILL INSTANTLY SELF DESTRUCT IF NOT WIRED CORRECTLY OR IF (+) & (-) ARE REVERSED!